## Slide 1
IoTtalk: A Platform for IoT Applications Quick Development
Dr. Yun-Wei Lin NYCU

## Slide 2: Outline
The Evolution of Communication
What and Why is IoTtalk?
How to deploy?
Device Connections with IoTtalk
IoTtalk System Architecture
Web-based IoT Applications
Conclusion

## Slide 3: The Evolution of Communication
H2H
A humans talks to the other humans.
H2M
A human directly controls the machines.
Machines have logic or intelligence to manipulate other machines. That is, IoT devices can talk to each other, IoTtalk!
M2M
A machine automatically controls the other machines.
The human manipulates the machine himself.
The human talks to the other humans.

## Slide 4: What is IoTtalk?
IoTtalk is an IoT device management tool
IoT management concept
  Device Feature
    The function or capability which an IoT can provide
  Device Model
    A set of device features
    A device model refers to a specific product
  Device name
    The name of a specific product
Feature 1
Feature 2
Feature 3
⁞
Model
An IoT device
Name
G-sensor
Mic.
Display
⁞
Smartphone
For example: Lin’s phone

## Slide 5: Why is IoTtalk?
Applications can simply develop with lower efforts
Simple and intuitive GUI
Application development without real devices is feasible

## Slide 6: Simple and Intuitive GUI
Connections by intuitional drawing links between IoT devices
Transparently observe the connections between IoT devices
Monitor the transmitting values between IoT devices
Application debugging is more easier

## Slide 7: Applications can simply develop with lower efforts
Reusable DF modules
  Even they are different IoT devices

## Slide 8: Application development without real devices is feasible
Do not need the real devices first to develop applications
The simulator provides the numerical values as inputs

## Slide 9: Easy to Deploy and Operate
Raspberry Pi4
Intel Edison
PC server
VMs in the Cloud
For example, you can try
https://demo.iottalk.tw

## Slide 10
Input Device
Features
Output Device
Features
Mic
Acc
Lum
Fan
Swh
Acc
Tmp
D1
D2
D3
1
2
3
4
NA1
NA3
D4
D5
NA2
ACC
Network Application NA1
ACC-IDF Module
LUM-ODF Module
D1
D3
LUM
Appliance Connections with IoTtalk

## Slide 11
Bulb
Smartphone
IoTtalk
Network Application
ODF
module
Service Logic Unit
IDF
module
normalization
scalar
scaling
ACC
LUM
Connection and Mapping Manner

## Slide 12: Connect Appliances to IoTtalk

## Slide 13: System Architecture
DAI
DAN
IoT Device
(Bluetooth/BLE/WiFi/...)
HTTP
(WiFi/3G/LTE)
HTTP
IoTtalk
IDA
Mobile Device
GUI
DA
HTTP
CSM
ORM API
CCM
Database
ESM
DA: device application
DAN: DA to Network
DAI: DA to IoT device
IDA: IoT DA
IDA: IoT DA

## Slide 14
ArduTalk - IoTtalk and Arduino Yun

## Slide 15
DAI
DAN
HTTP
(WiFi)
HTTP
IoTtalk
IDA
Arduino Yun
GUI
DA
HTTP
Comm.
ORM API
Config & Connect
Database
Execute
Linino AR 9331
ATmega32u4
Bridge
Wi-Fi AP
ArduTalk - IoTtalk and Arduino Yun
DA: device application
DAN: DA to Network
DAI: DA to IoT device
IDA: IoT DA
IDA: IoT DA

## Slide 16
IoTtalk
IoTtalk is a network application platform to simplify the network application development.
Cloud
IoTtalk
API
NA2
NA1

## Slide 17
OneM2M
NA1
API
NA2
If the device is developed under oneM2M, openMTC, or AllJoyn, these IoT platforms will provide APIs for the user to develop network application for the device.
Cloud
API

## Slide 18
AllJoyn
OneM2M
NA1
API
NA2
Cloud
NA3
API
These standards are difficult to interoperate, and the devices cannot easily communicate

## Slide 19
IoTtalk
IoTtalk is a network application platform built on top of the above IoT systems to simplify the network application development.
Cloud
OneM2M
AllJoyn
API1
API2

## Slide 20: The Smart Home Solution by CHT
CHT Wi-Fi dongle
Raspberry Pi 3/4
CHT IoT Gateway
(Wi-Fi)
(Wi-Fi)
(Wi-Fi)
CHT Appliance Remote APP
(Wi-Fi)
Chunghwa Telecom (CHT) provides a smart home solution through a USB dongle and an IoT gateway.
Each appliance is plugged in the USB Wi-Fi dongle for connecting to the IoT gateway.
A user can remote an appliance by its remote APP in the smartphone.
Smartphone

## Slide 21
Smartphone
IoTtalk
DA
(Wi-Fi)
Appliances
Sensors
(Wi-Fi)
CHT IoT
Gateway
DAI
DAN
WebSocket
HTTP
CSM
ESM
CCM
DB
GUI
DA:
1. Register/Deregister for appliances/sensors according to notifications
2. Pull commands from the IoTtalk server to CHT home server
3. Receive sensor data then Push them to the IoTtalk server
CHT-GW
Fan-O
CHT-Ctl (Remote)
Fan-I
Join 1
Remote
Smartphone
CHT APP
Remote
(Wi-Fi)
MorSensor1
Temperature
CHT Smart Home with IoTtalk
CHT-GW is the DM.
Each feature refers an appliance.
Cloud
Join 2
Smartphone
Remote
SW1
SW2
SW3
CHT IoT Gateway
For example:

## Slide 22
IoTtalk with Machine Learning
GridSearch

## Slide 23
Fan Control using IoTtalk
Click the device features of the two devices to create a link between them.
Then, the user controls the Fan using Keypad through IoTtalk
Remote
Fan
Remote
5
4

## Slide 24
Smart Fan using IoTtalk with Machine Learning
Insert a machine learning device and sensors between Keypad and Fan.
Machine learning device

## Slide 25: Conclusion
IoTtalk is an IoT device management tool
Easy to deploy and operate
Easy to develop applications - simply connect IDFs and ODFs
Transparently observe the connections between IoT devices
Monitor the transmitting values between IoT devices
Application debugging is more easier